Design Surface
Gary Herron & Frank Little
Locally, a surface is a 2D subset of 3D. Is means there is a 1 to 1 correspondence (homeomorphism) between each point of the surface and a point in 2D. Often, the surface is locally functional with respect to a plane, which constructs the homeomorphism implicitly. The smoothness of the surface is the differentiability of this implicit function. Implicitly Cn is Gn. An implicitly C1 or G1 surface is “smooth” and is characterized by a continuous unit normal.
When a smooth curve is in a surface, every derivative is in the surface. This transfinite property participates in the smoothness of the surface. When a smooth curve separates two surface patches which join G1, the surface normal is the cross product of the curve tangent and an independent surface tangent. Factoring smoothness: Two surface patches, that share a curve and its perpendicular tangent direction, join smoothly.
Cubic edges provide an effective tool for surface design. Vertices are connected by cubic segments that have no other intersections or terminations. Bezier provides a convenient design handle for the cubics. Linear interpolation of the perpendicular tangent direction is shared if tangents describe unique vertex normals. Expanding this to quadratic interpolation to a shared mid cross tangent or BARB is motivated by the quadratic derivative of the cubic edge.
A triangle is a 3 cycle of segments.
Herron’s 15 dof triangle: H_{ 15 } equiv C_ 9 -H_6 (I-C_9 ) over a triangle left (x , y right ) = sum from {i = 1} to {3} {{b} rsub {i}} {V} rsub {i}
C9 = sum from {i = 1} to {3} {{b} rsub {i} rsup {2} left ({left (3 − 2 {b} rsub {i} right ) F} rsub {i} + {b} rsub {j} {T} rsub {ij} + {b} rsub {k} {T} rsub {ik} right )} {T} rsub {ij} = ∇ {F} rsub {i} ∙ left ({V} rsub {j} − {V} rsub {i} right )
H6 = {{9 {b} rsub {1} {b} rsub {2} {b} rsub {3}} over {2} left lbrace sum from {i = 1} to {3} {{left (left (2 {b} rsub {k} − {b} rsub {j} right ) {X} rsub {kj} + left (2 {b} rsub {j} − {b} rsub {k} right ) {X} rsub {jk} right )} over {{b} rsub {i}}} right rbrace} over {sum from {i = 1} to {3} {{1} over {{b} rsub {i}}}} X_{jk} = {left none {∇ left (F − {C} rsub {9} right ) ∙ ∇ {b} rsub {i}} over {∇ {b} rsub {i} ∙ ∇ {b} rsub {i}} right rline} rsub {{left (2 {V} rsub {j} + {V} rsub {k} right )} / {3}}

Vertices and tangents define C9. The {X} rsub {jk} are determined from the interpolant to the perpendicular direction along the edge and the shape of any domain triangle.
 {left none {∂ {C} rsub {9}} over {∂ {b} rsub {1}} right rline} rsub {{left (2 {V} rsub {2} + {V} rsub {3} right )} over {3}} = {4 left ({∂ {b} rsub {2}} over {∂ {b} rsub {1}} {F} rsub {2} + {∂ {b} rsub {3}} over {∂ {b} rsub {1}} {F} rsub {3} right )} over {3} + {left ({4 T} rsub {21} + {T} rsub {31} − 4 {T} rsub {23} + left (3 {∂ {b} rsub {3}} over {∂ {b} rsub {1}} − 1 right ) {T} rsub {32} right )} over {9}
{∂ F} over {∂ {b} rsub {i}} ≡ {∇ F ∙ ∇ {b} rsub {i}} over {∇ {b} rsub {i} ∙ ∇ {b} rsub {i}}	{∂ {b} rsub {j}} over {∂ {b} rsub {i}} = {{e} rsub {j} ∙ {e} rsub {i}} over {{e} rsub {i} ∙ {e} rsub {i}}	ei=Vk-Vj.
{∇ {b} rsub {n}} over {∇ {b} rsub {n} ∙ ∇ {b} rsub {n}} = sum from {i = 1} to {3} {{∂ {b} rsub {i}} over {∂ {b} rsub {n}}} {V} rsub {i} is the nth altitude vector.
{left none {∂ {C} rsub {9}} over {∂ {b} rsub {1}} right rline} rsub {{left (2 {V} rsub {2} + {V} rsub {3} right )} / {3}} = {4} / {3} left ({∂ {b} rsub {2}} over {∂ {b} rsub {1}} {F} rsub {2} + {∂ {b} rsub {3}} over {∂ {b} rsub {1}} {F} rsub {3} right ) + {left ({4 T} rsub {21} + {T} rsub {31} − 4 {T} rsub {23} + left (3 {∂ {b} rsub {3}} over {∂ {b} rsub {1}} − 1 right ) {T} rsub {32} right )} / {9}
Let {N} rsub {jk} = {T} rsub {jk}-{T} rsub {ji}{{T} rsub {ji} ∙ {T} rsub {jk}} over {{T} rsub {jk} ∙ {T} rsub {jk}} be the perpendicular to the ith edge and let {n} rsub {jk} = {{N} rsub {jk}} over {left ldline {N} rsub {jk} right rdline} be the unit direction perpendicular.
(If nabla F_{j} is orthonormal then {N} rsub {jk} = {∇ {F} rsub {j} ∇ {b} rsub {i}} over {∇ {b} rsub {i} ∙ ∇ {b} rsub {i}} .)
Linear interpolation: n(s)=left (1 − s right ) {n} rsub {jk} + s {n} rsub {kj} .
 {left none {∇ F ∇ {b} rsub {i}} over {∇ {b} rsub {i} ∙ ∇ {b} rsub {i}} right rline} rsub {left (left (1 − s right ) {V} rsub {j} + s {V} rsub {k} right )} = left (left (1 − s right ) {n} rsub {jk} + s {n} rsub {kj} right ) left (left (1 − s right ) left ldline {N} rsub {jk} right rdline + s left ldline {N} rsub {jk} right rdline right ) ≡ {X} rsub {i} left (s right ) .

{X} rsub {i} left (1/3 right ) =X_{ jk} and {X} rsub {i} left (2/3 right ) =X_{ kj} . Replacing left (left (1 − s right ) {n} rsub {jk} + s {n} rsub {kj} right ) with left (left (1 − s right ) left (1 − 2 s right ) {n} rsub {jk} + 4 s left (1 − s right ) {B} rsub {i} + left (2 s − 1 right ) s {n} rsub {kj} right ) , a quadratic interpolant, uses the BARB, {B} rsub {i} , a mid-boundary cross-tangent. {B} rsub {i} is arbitrary but may be defaulted to {{n} rsub {jk} + {n} rsub {kj}} over {2} for the linear interpolant or may be modified for perpendicularity or unit length. Sharing {B} rsub {i} between patches maintains smoothness. left ldline {B} rsub {i} right rdline controls the fullness or tension of the surface.