Three points define a triangle. T =(V1,V2,V3)
Counterclockwise order means the triangle faces up or out. ijk is 123, 231, or 312. e_i equiv V_k - V_j .
A point in the triangle is a convex weighting of its vertices. V =sum from{i=1} to{3} b_{i} V_i b_1,b_2,b_3 >= 0 b_1+b_2+b_3 = 1
The scalar weight of each vertex point is its barycentric coordinate.
Barycentric coordinates map all triangles to each other.

In 2D,	b_i = left lline binom V-V_j V_k-V_j right rline /left lline binom V_i-V_j V_k-V_j right rline = 2A_i / 2A= (V-V_j) cdot e_i rsup L / 2A e_i rsup L =( y_j-y_k,x_k-y_j )
nabla b_i , is perpendicular to e_i . { nabla b_i } over {ldline nabla b_i rdline rsup 2} is the ith height vector.

The symbol { partial F} over { partial b_{i} } is defined as lim from{ %delta rightarrow 0} {{F(b_{i}+%delta) } over {%delta} } where every thing else is held constant.
This can’t be done here, b_1+b_2+b_3 = 1 , so the symbol needs definition. { partial F} over { partial b_{i} } equiv {nabla F cdot nabla b_i } over { nabla b_{ i } cdot nabla b_{ i } } .
{partial b_{j}} over { partial b_{i}}= { e_j cdot e_i } over {e_i cdot e_i}	sum from{i=1} to{3} b_{i}=1 and { partial b_{i}} over { partial b_{i} }= 1 so {partial b_{j}} over { partial b_{i}} +{partial b_{k}} over { partial b_{i}} = -1 .
The 6 numbers, left lbrace { partial b_j } over { partial b_i } right rbrace , define the shape of a triangle with 2 degrees of freedom.
{partial b_j }over {partial b_i} = -1/2 ,j <> i describes an equilateral triangle.
A uniform partition can be used as the domain for a simple piece-wise defined curve.
A simple piece-wise defined surface can use all equilateral triangles for its domain.
A chord length partition improves the shape of curves.
Applying {partial b_{j}} over { partial b_{i}}= { e_j cdot e_i } over {e_i cdot e_i} to the range triangle improves the shape of surfaces.